## Slide 1
🛡️
COMPUTER NETWORKS
Name: Rohit Raj
Class: B.tech cse aiml - C
Roll no.: 2301730179
Topic : Firewall

## Slide 2
01 | INTRODUCTION
What is a Firewall?
A firewall is a network security device or software that monitors and filters incoming and outgoing network traffic based on an organisation's previously established security policies.
⬥ Acts as a barrier between a trusted internal network and untrusted external networks (e.g., the Internet)
⬥ Inspects data packets and decides whether to allow or block them based on predefined rules
⬥ Can be hardware-based, software-based, or a combination of both
⬥ Operates at different layers of the OSI model depending on the type
⬥ First line of defence in any network security architecture
🔒

## Slide 3
02 | CLASSIFICATION
Types of Firewalls
🧱 Packet Filtering
⬥ Works at Network Layer (L3)
⬥ Checks source/dest IP & port
⬥ Fast but limited inspection
⬥ Stateless — no context
🔗 Stateful Inspection
⬥ Tracks active connections
⬥ Maintains state table
⬥ Context-aware decisions
⬥ Stronger than packet filtering
🌐 Proxy / Application
⬥ Operates at Application Layer (L7)
⬥ Deep packet inspection (DPI)
⬥ Content filtering capabilities
⬥ Higher latency, higher security
☁️ Next-Gen Firewall (NGFW)
⬥ Combines traditional + advanced
⬥ Intrusion prevention (IPS)
⬥ Application awareness
⬥ Threat intelligence feeds
🖥️ Software vs Hardware
⬥ Software: installed on OS/host
⬥ Hardware: dedicated appliance
⬥ Cloud-based options growing
⬥ Often combined in practice

## Slide 4
03 | MECHANISM
How Firewalls Work — Advantages & Limitations
⚙️ Working Mechanism
⬥ Incoming packet arrives at firewall interface
⬥ Headers inspected: source IP, dest IP, port, protocol
⬥ Packet compared against Access Control List (ACL) rules
⬥ Rules evaluated top-down; first match determines action
⬥ Action: ALLOW, DENY, or LOG the packet
⬥ Stateful firewalls also check connection state table
✅ Advantages
⬥ Prevents unauthorized access to private networks
⬥ Blocks malicious traffic & known attack patterns
⬥ Enables centralized security management & logging
⚠️ Limitations
⬥ Cannot protect against internal (insider) threats
⬥ Encrypted traffic may bypass inspection
⬥ Complex rule sets can cause misconfiguration
⬥ Does not replace antivirus / endpoint security

## Slide 5
04 | CONCLUSION
Key Takeaways & Conclusion
🛡️ Defence Layer
Firewalls are the essential first line of defence, filtering traffic between trusted and untrusted networks.
🔍 Evolving Tech
From simple packet filters to NGFWs with AI-driven threat intelligence, firewall technology continues to evolve.
🔐 Layered Security
Firewalls alone are not enough — they must be part of a defence-in-depth strategy alongside IDS, IPS, and endpoint security.
"A firewall is not a silver bullet, but without it you are shooting in the dark."
Thank You